## Slide 1: Balancing Shipboard Energy with Warfighting Needs
Marine High Power Battery Workshop: Electric/Hybrid Vessel
15 Dec 2016
John Heinzel, Ph.D
Naval Surface Warfare Center, Philadelphia Division

## Slide 2: Don’t Ships Have Lots of Power?
DDG-51 Flight 2A:
~9MW installed electric power; ~75MW installed mechanical propulsion
DDG-1000: ~78MW installed electric power
Accessing Power is Key…

## Slide 3: Shipboard Electrical Power to Meet Mission Loads
Adapted from http://www.navsea.navy.mil/Portals/103/Images/TeamShips/PEOShips/ESO/Integrated_Architectures_figure2ex.jpg
Integrated
Architectures
Traditional
Architectures
Extra
Power Available to
Loads

## Slide 4: Leveraging ALL Installed Power
Prime
Mover
Generator
Main Power
Distribution
Power
Conversion
Module
Ship
Service
Power
Motor
Drive
Propulsion
Motor
Mission
Loads
Power
Conversion
Module
Power availability by ensuring all prime movers are accessible to all loads offers:
Additional and larger mission loads
Power flexibility and optimization of plant loading
Enhanced survivability if reconfigurable

## Slide 5: Gas Turbine Generator Transient Response
Single-Spool Engine
Example: DDG 51 Allison Generator
Multi-Spool Engine
Example: DDG 1000 MT-30
Efficiency @
Part Load
Load Response
Availability @
>10MW
Aerodynamic couple in two-spool GTG
makes transient concerns greater; however,
available large GTGs all use this architecture.
Accessing Power is Key…Not just the ratings
Makes energy storage buffers necessary…

## Slide 6: Energy Storage: A Means to Get Fuel Savings and Operational Capability
Single Generator Operations (Shipwide UPS)
Generator load optimization/scheduling
Minimization of spinning assets
Terrestrial distributions (microgrids)
Online storage devices for backup power
UPS for protection of sensitive devices
Closed, signature-free energy source
Energy Surety
Fuel Savings
Power Quality
Advanced Loads
Advanced GTG Transient ridethrough
Load changes outside of design space for prime movers
Pulsed applications
Highly transient loads
Cyclic load requirements
Increasing UPS and Batteries
Potential EMRG Load Profiles
Power Quality Surety Under Two-Spool GTG Application

## Slide 7: Future Operational Mode
Load Profile
Generator
Adv. Energy Storage
+
Continuous Generator loading
Power Generation Free to Operate at Most Fuel Efficient, Reliable Level
Multi-Device Energy Storage Sized for Peak and Continuous Ride Through
Mil Std Power Quality
Optimize storage buffering prime movers to enable continuous Directed Energy Weapons operations with optimized, efficient loading of spinning assets…
Peaky Loads

## Slide 8: Energy Storage Approaches
Batteries
Hybrids
Flywheels
Typically Lithium-Iron Phosphate for Shipboard use
Future innovations welcome
High power, low impedance variants necessary; Power density and thermal performance emphasized
Safety behaviors are critical
Solid BMS and sensing
Battery-Capacitor; Battery-Flywheel and Battery-Battery variants offer benefits in various applications
Supports high rate and high ripple/noise applications
Superior dispatch characteristics
Mix and match at the LRU level
Scales with square of rotational speed, which enables density advantages
Efficiency, thermal management and safety are critical
Advanced materials and shock tolerant designs are desirable to ensure life and performance

## Slide 9: Assessment of Current Tech
Technology
Standard Unit Power/
Energy Level
Technology Readiness Level
Challenges
Non-Sub Weight, Longevity,
VRLA Battery 2.4kW/1kWh 9 Power Density
Large-Format Safety, High
Li-ion Battery 10kW/2kWh 4+ Temperature Ops
Advanced Capacitor 1.5kW/.0021kWh 4+ Energy Density
(single) Controls/Interface
Flywheel 25kW/4kWh 4 (~7 EMALS) Shock/Vibe/
Parasitics
Na Battery 33kW/14kWh 4 TBD
The Navy has active efforts in all of these technology areas and more

## Slide 10: Li-ion Baggage…
787 APU Battery (NTSB.gov)
EV Fires (NFPA.org)
Consumer Electronics (wired.com)
Li-ion Cargo (NTSB.gov)

## Slide 11: Safety is Paramount
Chemistry Selection
Engineering design and controls
Abusive testing and mitigations
Unique NAVSEA 9310, MIL-882 and SG-270 analyses and safety packages

## Slide 12: LFP for Medium-Rate Ops
Super Capacitor
Ni-MH
High Power Li-ion
Medium Power Li-ion
High Energy Li-ion
Very-High Power Li-ion
Ultra-High Power Li-ion
AgO-Zn
High Energy LFP
High Power LFP
Target operational
P/E Ratio and C-rate
~20% Energy Density Reduction for Increase in Safety

## Slide 13
Battery Safety: Heat Release
Under Abuse/Failure
LFP Minimal Heat Release at Elevated Temps
Courtesy: Saft
Courtesy: SNL
Electrolyte, separator and negative electrode are still thermal contributors
Minimal positive electrode contribution
Lithium Iron Phosphate (LFP) Optimal Near-Term Selection
Li-ion Chemistry for Power, Impedance and Safety

## Slide 14: Combined Electric Ship With Storage
Higher Efficiency of Power Utilization for Electrical and Propulsion Loads
Source: Doerry et. al, 2010
Optimization of Plant Genset
Lineup and Loading
Future High-Efficiency Sources, e.g. Fuel Cells
Plant Efficiency + Power Accessibility = Efficient , Available Power
that is part of the Kill Chain
+
=
Storage Components
Integration and Control
SEA 05D Rendition of a Notional Next-Generation Flex-Ship
Active Decision Making

## Slide 15: Opportunities for Industry Innovation
Safe, common, affordable batteries, capacitors, flywheels and other storage innovations
Compact and efficient power conversion
Innovative means of managing highly transient loads
New approaches to improve engine (diesel & GT) response rates
Thermal management
Commonality

## Slide 16: Conclusions
Present and emerging threats will continue to increase the electrical power demand on warships
Considered management of generation, quality, and load will enhance the ability of the warfighter to fight, indeed, perhaps enable the fight
The ideal power management architecture will harness all installed power yet provide the maximum flexibility
  Margin in the form of quantity
  Flexibility to quickly switch electrical power use between propulsion, weapons, sensors and more

## Slide 17
QUESTIONS?