## Slide 1: Class Rules for Battery Powered Vessels
Marine Hi-Power Battery Workshop MARAD

## Slide 2: DNV GL Classed and pre classed vessels with batteries

## Slide 3: Sec.1 Battery Power
1 General................................................................................................. 10
  1.1 Introduction....................................................................................... 10
  1.2 Terminology and definitions................................................................. 11
  1.3 Procedural requirements......................................................................12
2 Design principles for Battery(Safety) notation..................................... 15
  2.1 General............................................................................................. 15
  2.2 Arrangement......................................................................................15
  2.3 Operational environment control...........................................................15
  2.4 Fire safety for battery spaces.............................................................. 17
  2.5 Safety assessment..............................................................................18
  2.6 System design................................................................................... 18
  2.7 Testing.............................................................................................. 19
  2.8 Operation and maintenance................................................................. 19
3 Design principles for Battery(Power) notation..................................... 19
  3.1 General............................................................................................. 19
  3.2 System design................................................................................... 20
  3.3 Testing.............................................................................................. 21
  3.4 Operation and maintenance................................................................. 21
4 Battery system..................................................................................... 21
  4.1 Battery system design........................................................................ 21
  4.2 Testing.............................................................................................. 23Content
Part 6 Chapter 2 - Propulsion, power generation and auxiliary systems

## Slide 4: 2 Design principles for Battery(Safety) notation
Part 6 Chapter 2 - Propulsion, power generation and auxiliary systems
Battery(Safety) (a new notation in 2015) A notation that cover requirements for the safety of the battery installation covering vessel arrangement, environmental control including temperature and ventilation.
To prevent thermal incidents in battery spaces, then the rules gives requirement to fire integrity, detection and extinguish measures.
=
~
G
=
~
G
~
~
~
~
~
~

## Slide 5: 3 Design principles for Battery(Power) notation
Battery (power) The notation you need when the battery is used as a main source of power (propulsion power).
The rules put requirements for redundancy and location. In addition the time or range that the battery can supply energy shall be calculated taken into account the planned operation/voyage
~
=
=
~
=
~
Part 6 Chapter 2 - Propulsion, power generation and auxiliary systems

## Slide 6: 2 Design principles for Battery(Safety) notation
Location of battery space [2.2]
  Aft of collision bulkhead
  Structural integrity
  Limitation of other equipment
  No heat sources or high fire risk objects
Part 6 Chapter 2 - Propulsion, power generation and auxiliary systems

## Slide 7: 2 Design principles for Battery(Safety) notation
Environment (ventilation, temperature) [2.3]
  Temperature control
  Ventilation (normal and emergency)
  Possible hazardous area (explosion risk)
Part 6 Chapter 2 - Propulsion, power generation and auxiliary systems

## Slide 8: 2 Design principles for Battery(Safety) notation
Fire safety [2.4]
  Defines as other machinery space according to SOLAS
  Fire integrity A60 and A0
  No thermal propagation in battery system
  Fire detection
  Fire extinguishing
Part 6 Chapter 2 - Propulsion, power generation and auxiliary systems

## Slide 9: 2.5 Safety Assessment
Part 6 Chapter 2 - Propulsion, power generation and auxiliary systems
Conformance and non-conformance with the requirements in [2.2], [2.3] and [2.4] shall also be included in
the safety assessment.
Rule paragraph | Conformance | Description
[2.2.1] | YES | Battery space in container on main deck
[2.2.2] | YES | Battery space contains only battery system
[2.2.3] | YES | There are no heat sources in battery space
[2.3.1.1] | NO | Battery system is liquid cooled
[2.3.1.2] | … | …
[2.3.1.3] | … | …
[2.3.1.4] | … | …
[2.3.1.5] | … | …
… | … | …
[2.4.3.2] | YES | …

## Slide 10: 2 Design principles for Battery(Safety) notation
System design [2.6]
  Short circuit and overcurrent protection
  Isolating switch gear
Testing [2.7]
Maintenance [2.8]
Part 6 Chapter 2 - Propulsion, power generation and auxiliary systems

## Slide 11: 3 Design principles for Battery(Power) notation
Battery (power) The notation you need when the battery is used as a main source of power (propulsion power).
The rules put requirements for redundancy and location. In addition the time or range that the battery can supply energy shall be calculated taken into account the planned operation/voyage
~
=
=
~
=
~
Part 6 Chapter 2 - Propulsion, power generation and auxiliary systems

## Slide 12: 3 Design principles for Battery(Power) notation
System design [3.2]
  2 independent battery systems (only batteries)
  Cable routing
  Selectivity
  Local operation
  Energy management system
Testing [3.3]
Operation and Maintenance [3.4]
Part 6 Chapter 2 - Propulsion, power generation and auxiliary systems

## Slide 13: 3.2.3 Energy Management System, EMS
Energy Management System (EMS) shall be installed.
Control battery temperatures by:
  Limiting charge and discharge current.
  Limiting max and min battery voltages.
Monitor:
  available energy of the batteries
  remaining time or range that the battery can supply energy for the planned operation/voyage
  state of health of the batteries (SOH)
Alarms related to capacities.
Part 6 Chapter 2 - Propulsion, power generation and auxiliary systems
EMS

## Slide 14: Sec.1 Battery Power
http://rules.dnvgl.com/docs/pdf/DNVGL/RU-SHIP/2016-07/DNVGL-RU-SHIP-Pt6Ch2.pdf
Part 6 Chapter 2 - Propulsion, power generation and auxiliary systems

## Slide 15: 4 Battery System
Safety description
  Potential gas development (volume)
  Fire risk
  Submersion
  Explosion
  Detection
  Extinguishing
  Thermal runaway, internal cell failure
  External fires/hazards
  Safe charge/discharge characteristics
Part 6 Chapter 2 - Propulsion, power generation and auxiliary systems

## Slide 16: 4.3.1 Battery Management System
Integrated BMS
  Control
  Protect
  Monitor
  Alarms
    Abnormal conditions
  Calculate (SOC, SOH)
Independent emergency disconnect
Independent temperature shutdown
Testing
  Safety
  Functionality
BMS
Part 6 Chapter 2 - Propulsion, power generation and auxiliary systems

## Slide 17: Sec.1.[4.2] Testing
Part 6 Chapter 2 - Propulsion, power generation and auxiliary systems

## Slide 18: Class Rules for Battery Powered Vessels
DNV GL Maritime Classification
MCANO381@dnvgl.com
+47 67578665