## Slide 1
2016 MARAD Battery Workshop
ABS Class Requirements for Li-Ion Battery Installations
Michael Roa | December 15-16, 2016
2016 MARAD Battery Workshop

## Slide 2
Summary of ABS Rules being considered for Commercial Vessels
  Drawings and details to be submitted for review and approval
  Overload and short circuit protection settings
  Installation arrangements to be submitted
  Battery location to be evaluated
  Ensure protection of crew, environment and surroundings
  Maintenance schedule
  Material Safety Datasheet
  Nameplate information
  Operations and maintenance manual
  Battery Management System functional testing
  Independent Emergency Shutdown from navigation bridge and outside space
  Installed in well ventilated, environmentally controlled space
  High ambient temperature alarm in compartment
  Fire extinguishing system – medium to be suitable for battery chemistry
  Fire safety measures recommended by battery system manufacturer
  Suitable Ingress Protection (IP) enclosure rating
ABS Class Requirements Under Development for Li-Ion Installations

## Slide 3
Additional criteria for large battery installation serving electric propulsion, essential and/or emergency services:
  HAZID/HAZOP analysis
  Detailed risk analysis
  Unit certification required for batteries serving:
    Electric propulsion
    Essential and/or emergency services
  Structural fire protection for battery room
  Fire and gas detectors and alarms
  Manufactured under an approved quality assurance program
ABS Class Requirements Under Development for Li-Ion Installations

## Slide 4
Component Design Failure Modes and Effects Analysis (DFMEAs)
Design Verification Test Plan report (DVTP) to verify the DFMEA
Battery component Risk Analysis document (FMEA, HAZID, etc.)
Environmental Type Test reports per ABS 4-9-8/Table 1
Test reports for the battery cells per recognized standard (UL 1642)
Unit Certification test reports 4-9-8/Table 2 (ABS Surveyor witness )
Battery management system functional test report (witness by ABS)
Battery technical specifications and Material Safety Data Sheets
Functional description of operating modes of the battery pack
Control & monitoring system functional description/safety philosophy
Appropriate service experience and usage history of the battery
Plans and Data for Li-ion Battery Components

## Slide 5
Lithium-ion battery design approval documentation
Unit Certification test reports, in accordance with 4-9-8/Table 2
Battery management system functional test reports (ABS witness)
Battery pack capacity, Battery Installation wiring schematic drawing
Battery storage location and arrangement plan
Battery System Risk Analysis document
Sea-trial/commissioning safety procedures
Ventilation arrangement of space, Environment control arrangement
Fixed Fire protection arrangement
Combustible Gas detection arrangement
Emergency Shutdown Arrangement
Battery Installation/Mounting arrangement – weights, connection details
Hazardous Area Classification drawings, if applicable.
Maintenance schedule and procedures of battery replacement
Operations & maintenance manual for battery & BMS
Plans and Data for Li-Ion Battery Installations

## Slide 6
At a minimum, must address the following risks and the mitigation techniques used by the battery manufacturer to prevent each of these risks from developing into dangerous situations:
  Thermal Runaway
  Over-Current
  Over-Voltage/Under-Voltage
  Cell-Balancing
  External and Internal Electrical short-circuit
  Temperature measurement sensor failure
  Individual cell voltage measurement sensor failure
Battery Component Risk Analysis

## Slide 7
Battery System Risk Analysis document must address:
  External heating: Appropriate measures taken in the design of the battery space to prevent the possibility of thermal runaway due to external heating of the battery modules/pack, for example, through the use of fire-rated barriers, fire-suppression systems (based on recommendation from battery manufacturer), etc.
  External risks: Appropriate measures taken to account for external hazards, such as possible fire, flood, explosion risks, etc.
  Loss of communication with external power management system on-board vessel: Appropriate measures taken to isolate the battery pack in the event of a loss of communication with the power management system on board the vessel
Battery System Risk Analysis

## Slide 8
Battery casing is made of flame-retardant material
Battery modules designed to contain any thermal damage or fire
BMS control and protection functions
BMS redundancies and communication protocols used
Maintenance schedule and procedures of battery replacement
Means to prevent spilling of electrolyte
Size of the connecting cable and protection arrangement
Outgoing circuits protected against overload and short circuit
Emergency battery packs not installed in emergency switchboard space
Mechanism for electrical isolation for maintenance purposes
Battery module pressure-relief mechanism to vent gas to atmosphere.
Operations and maintenance manual includes normal and emergency operating procedures and maintenance procedures
Battery and Battery Management System

## Slide 9
Emergency shutdown adjacent but outside of the battery space/room
Emergency shutdown on navigation bridge for propulsion batteries
Alarms provided at continuously manned location for:
  Cell over-voltage
  Cell under-voltage
  Cell over-temperature
  Battery pack ground fault
  Failure of communication with external power management system/control system
  High ambient temperature in battery space
  Tripping of battery fuses/contactors that electrically isolate the battery pack
  Failure/shutdown of the battery pack or failure of any of the individual modules/battery components
Battery System Alarms and Shutdowns

## Slide 10
Battery Management System
  Relevant software/hardware design requirements for a Category II computer based systems
Rating
  Battery components designed for continuous operation at rated capacity (during discharge) at the ambient temperature of space per 4-1-1/Table 8
Ventilation arrangement
  Ventilation system must safely dissipate resultant gases from an abnormal situation to the weather
Fire-fighting system
  Recommended by the battery manufacturer based on the battery chemistry used and in compliance with ABS Class requirements
Hazardous Area
  In the event that the battery space is considered a hazardous area, the requirements in 4-8-4/27.5.3 should be applied (armored cable, certified-safe electrical equipment, non-sparking fans, etc.)
Safety Measures

## Slide 11
Battery storage location and arrangement plan
  Should clearly show the battery pack arrangement with respect to the space it is being installed in
  Should show the clearance distances between the other equipment in the room and the battery pack
  Should show that the safety of the crew/vessel and firefighting systems effectiveness are clear (i.e. egress route, fire detector locations, fire-fighting system range/coverage, etc.)
Battery Compartment Arrangements

## Slide 12
Battery pack installation and sea-trial/commissioning procedures
  Testing of the following safety functions and associated alarms
  Cell Balancing detection/protection, Over-voltage detection/protection, Under-voltage detection/protection, Emergency shutdown arrangement, Ground-fault detection, Loss of communication detection/protection
  In each of these fault scenarios, the Surveyor is to be able to witness the battery pack being electrically isolated from the rest of the power system
Testing of the expected performance function/s of the battery pack on the particular vessel, for example functional tests for peak load sharing, blackout recovery, etc. to be performed during commissioning and/or sea-trials
Testing of the protective functions in the battery space, as applicable to the vessel specific installation
Safeguards in place to make sure that vessel operator is unable to continue using the battery pack whilst ignoring fault alarms
Sea-trial Testing and Commissioning Procedures

## Slide 13
Lithium Batteries - General Requirements
  Considered on a case-by-case basis for specialized applications
  Not permitted on passenger submersibles
  Certified by third-party independent agency to a recognized standard:
    NAVSEA S9310-AQ-SAF-010, US Navy Technical Manual for Batteries
    UL 1642, UL Standard for Safety of Lithium Batteries
    Section 38.3, UN Manual of Tests and Criteria
  Fabricated under an approved quality assurance program
  Appropriate service experience or test data
  Detailed risk analysis is to be carried out for evaluating and mitigating potential risks
ABS Rules for Underwater Vehicles and Hyperbaric Facilities

## Slide 14
Lithium Batteries – Installation on Manned Applications
  located outside pressure hull in pressure resistant battery pods
  Battery pods mechanically protected from direct impact loads
  Avoid compressed gas cylinders, windows, heat sources
  Suitable distance from the pressure hull in event of fire
  Means provided for jettisoning battery pods in the event of fire
  Battery pods provided with appropriate fire detectors and temperature sensors with audio-visual alarms at control station
  Pressure boundary of pressure resistant battery pods is to meet the A-60 class fire resistance rating
  Pods labeled appropriately and are to be provided with appropriate signs warning personnel against inadvertent abuse of the pods
ABS Rules for Underwater Vehicles and Hyperbaric Facilities

## Slide 15
Lithium Batteries –Battery Management System (BMS)
  Electronic battery management system (BMS) to provide for:
    Battery monitoring
    Charge control to prevent cell overcharging/undercharging
    Discharge control to prevent cell over-discharging
    Inter-module and intra-module balancing of the cells
    Monitor voltages, currents, state of charge, and temperatures at the battery cell and module levels
    Alarms at control station for parameters outside limits
  BMS is to be certified by the manufacturer
  Operations and Maintenance Manuals
  Charging - Not at sea, Charging of lithium batteries is to be carried out using the chargers specified by the battery manufacturer
  Replacement – same manufacturer at required intervals
ABS Rules for Underwater Vehicles and Hyperbaric Facilities

## Slide 16
Li-Ion batteries have unique hazards
Sufficient safeguards needed for large-scale marine applications
Material selection, electrolyte chemistry, casing design and Battery Management System design, and must be carefully considered for the intended application
Thorough testing of both the battery and Battery Management System hardware and software should be conducted by the manufacturer in accordance with recognized industry standards
Larger batteries for use in essential services should be required to have a unit certification
ABS has set in place specific internal guidelines to be followed for Lithium-Ion battery installations on commercial vessels
ABS is also in the process of developing detailed rules for marine applications in order to address the safety concerns associated with these battery technologies
Conclusion

## Slide 17
www.eagle.org
Thank you